## Slide 1
Team 11: Low-cost sensor for seamless road quality monitoring
Team: Yuhang Chen, Zhengwei Dai, Yichen Li, Yihang Yang
Goal: Utilizing the information collected by the sensors on vehicles to monitor the real-time road quality

## Slide 2
SMART goals
4.3
Sensor testing
Server design
Survey for filtering subsystem and feature extraction
4.10
4.17
5.1
Sensor testing
WIFI module building
Survey for segmentation subsystem and classification
Build the PCB board
Implement the data process on server
Send signal from PCB to server
Get familiar with sensor IO
Establishing connection
Start server implementing

## Slide 3
Tasks
Sensor
Server
Filtering
Feature extraction
Purchase and check the model and PIN of each sensor is correct
Test the data output of each sensor on the bread board
Connect the sensors to MCU and test data transmission
Step1. Connect ESP8266 with Stem32
Step2. Initialize ESP8266 Model: AP and STA mode
Step3. Establish TCP/IP and use python socket to build TCP/IP
Step4. Use python flask and html to build the HTTP server
Step5. Sent data from Stem32 by IP address
FFT to analyze the overall situation of the road. (roughness)
DWT to analyze the problems happen in part of the road. (normal, pothole, and transverse)
1. Apply fft to observe cut-off frequency of sensors
2. Low-pass filter for acceleration+ High-pass filter for angular velocity
3. Attitudinal Data Calculation with
Linear Kalman Filter
First Order Complementary Filter