## Slide 1
Team 11: Low-cost sensor for seamless road quality monitoring
Team: Yuhang Chen, Zhengwei Dai, Yichen Li, Yihang Yang
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB974DA658112395338783245C025A59995FB9E16632CCFAA0B432708CE5F45C8C42BB719BDFBEC94DA7A649C287EAE079169C97C71560C476F719A25EEB755DC5

## Slide 2
part 01
Introduction
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB974DA658112395338783245C025A59995FB9E16632CCFAA0B432708CE5F45C8C42BB719BDFBEC94DA7A649C287EAE079169C97C71560C476F719A25EEB755DC5
part 02
Design Overview
part 03
Implementation
In Detail
part 04
Analysis

## Slide 3
Part 01
Introduction
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB974DA658112395338783245C025A59995FB9E16632CCFAA0B432708CE5F45C8C42BB719BDFBEC94DA7A649C287EAE079169C97C71560C476F719A25EEB755DC5

## Slide 4
Member Introduction
Zhengwei Dai EE
01
03
02
04
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618
PCB design
Sensor testing
Yuhang Chen ECE
Server design
Establishing Connection between PCB and server
Yihang Yang ECE
Preprocessing algorithm design
Display design
Yichen Li ECE
Classification algorithm design
Dataset collection and labelling

## Slide 5
Introduction to Project
Brief Summary
We will build Low-cost road quality monitoring pipeline for Road Management and Maintenance Company and vehicle owners.
Problem
The road quality monitoring is not real-time and expensive. The traditional road monitoring is carried out regularly through special vehicles, which needs a lot of cost.
Solution
Designing a device which can be placed on a bicycle or vehicle to transmit the position information and corresponding sensor data to the server in real time.

## Slide 6
Part 02
Design Overview
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB974DA658112395338783245C025A59995FB9E16632CCFAA0B432708CE5F45C8C42BB719BDFBEC94DA7A649C287EAE079169C97C71560C476F719A25EEB755DC5

## Slide 7
High-level requirements
Sensitivity of accelerometer
When the measurable range is ± 2g, the sensitivity of the accelerometer should be greater than 10000LSB to ensure the accuracy of data measurement.
High-precision module
The server needs a high-precision module to eliminate the sensor noise signals caused by the vehicle itself, such as acceleration, deceleration or turning, so as to provide high-precision road conditions.
Fast transmission
The data transmission between monitoring device and server, server and mobile application should be completed within 500 milliseconds to ensure the real-time and effectiveness of road condition data.
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618
Fast analysis
The analysis of signal from accelerometer in the server should be completed within 0.2 seconds. It ensures the real-time and avoid the server will overload when processing great amount of data.

## Slide 8
Block Diagram
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618

## Slide 9
Part 03
Implementation
In Detail
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB974DA658112395338783245C025A59995FB9E16632CCFAA0B432708CE5F45C8C42BB719BDFBEC94DA7A649C287EAE079169C97C71560C476F719A25EEB755DC5

## Slide 10
Power Supply
GPS
Accelerometer
Wi-Fi
MCU
PCB Board

## Slide 11
Device Schematic

## Slide 12
Two 5V Batteries -- Power supply
One voltage regulator --convert input to 3.3V
Power Supply System
Requirement | Verification
The batteries should hold sufficient capability to support the hold system work | We need to check the batteries’ capability to ensure that the available working time of power supply should exceed the time for a vehicle’s test period on a road
The power module could support all the voltage supply requirement of the sensor components | With two 5V Batteries and a voltage regulator, the power module could provide voltage of 5V and 3.3 V, which is the voltage requirement of the modules in PCB
The set position of power module should be arranged properly | To avoid sliding or poor connection when the vehicle is driving, the power supply subsystem should be fixed well somewhere near the PCB
1
Requirement & Verification

## Slide 13
Control Module
2
MCU: use STM32F103C8 controller to receive the data from the accelerometer and GPS module and send the data to the backend service using Wi-Fi module.
Pin Diagram

## Slide 14
Serial Port | Pins | Tolerant
Serial1 (TX1,RX1) | PA9,PA10 PB6,PB7 | 5V
Serial2 (TX2,RX2) | PA2,PA3 | 3.3V
Serial3 (TX3,RX3) | PB10,PB11 | 5V
Tolerance
Requirement & Verification
Requirement | Verification
The control module could capture data from the sensors and check if sensor readings are within certain thresholds | If the data is not in rational range, the connected LED would turn into red to indicate a failed status in receiving data
The control module should work well with the WIFI module to enable the connection to the cloud server | The control ship should ensure the data transmitted correctly from the sensors to the cloud server by WIFI module with no data missing
The control ship mush have enough pins to support all the sensors and module we need | The control ship should have at least 2 pins for power supply, 6 pins for WIFI module, 4+8=12 pins for the sensors. Totally minimum pin number is 20
2
Control Module

## Slide 15
Wi-Fi Module
Wi-Fi module: use ESP8266 Wi-Fi module to connect MCU to the internet and send data to a webpage hosted on ESP8266 webserver.
Pin Number | Pin Name | Verification
1 | GND | Ground (0 V)
2 | TXD | Transmit data bit X
3 | GPIO 2 | General-purpose input/output No. 2
4 | CH_PD | Chip power-down
5 | GPIO0 | General-purpose input/output No. 0
6 | RST | Reset
7 | RX | Receive data bit X
8 | VCC | Voltage (+3.3 V)
3
Pin Description

## Slide 16
Wi-Fi Module
ESP8266 | STM32
VCC | 3.3V
GND | G
CH_PD | 3.3V
TX | PA3
RX | PA2
Pin Connection
3
Circuit diagram between ESP8266 and MCU
Tolerance
Input voltage | VDD: 2.5V to 3.6
Working Current | 80mA
Work Temperature | -40°C to+125°C

## Slide 17
Wi-Fi Module
Requirement | Verification
The WIFI module could interface with the MCU to allow varieties of data to transmit to the server | Working frequency of this module should be consistent with Mini controller. The pins of WIFI module and the pin of MCU could be linked properly to allow the WIFI module work properly (Voltage, Groud, Ports for data sent and received etc)
The ESP8266 would be programmed to run a HTTP server | we can communicate over the cloud server to the backend service by transmitting the data in the required format
Requirement & Verification
3

## Slide 18
NEO-6M GPS Module
Pin Number | Pin Name | Verification
1 | GND | Ground (0 V)
2 | TX | Transmit data bit X
3 | RX | Receive data bit X
4 | VCC | Voltage (+3.3 V)
NEO-6M GPS module: use the TinyGPS library to get data we need, such as latitude, longitude and altitude along with time. It connects to MCU to transmit the data.
4
Pin Description

## Slide 19
NEO-6M GPS Module
NEO-6M | STM32
GND | G
TX | PA9
RX | PA2
VCC | 3.3V
Requirement | Verification
The batteries should hold sufficient capability to support the hold system work | We need to check the batteries’ capability to ensure that the available working time of power supply should exceed the time for a vehicle’s test period on a road
Input voltage | 3.3 – 5.5V
Power Dissipation | 50mA
Work Temperature | -40°C to+85°C
Storage Temperature | -55°C to+100°C
Pin Connection
Requirement & Verification
Tolerance
4

## Slide 20
Accelerometer Module
MPU-6050 module: collect acceleration signal data in 3 directions to provide data for evaluating road quality. It also integrates 3-axis gyroscope and connects with MCU through IIC interface.
5

## Slide 21
Accelerometer Module
Pin Number | Pin Name | Pin Description
1 | CLKIN | Optional external reference clock input.
6 | AUX_DA | I2C master serial data, for connecting to external sensors
7 | AUX_CL | I2C master serial clock, for connecting to external sensors
8 | VLOGIC | Digital I/O supply voltage
9 | AD0 | I2C Slave Address LSB (AD0)
10 | REGOUT | Regulator filter capacitor connection
11 | FSYNC | Frame synchronization digital input.
12 | INT | Interrupt digital output (totem pole or open-drain)
13 | VDD | Power supply voltage and Digital I/O supply voltage
18 | GND | Power supply ground
20 | CPOUT | Charge pump capacitor connection
23 | SCL | I2C serial clock (SCL)
24 | SDA | I2C serial data (SDA)
Tolerance
5
Pin Description
Input voltage | 5V
Power Dissipation | 150mA
Current for IO | 25mA
Storage Temperature | 0°C to+50°C

## Slide 22
Accelerometer Module
Requirement | Verification
Control the temperature between 0 ℃ and 40 ℃ to ensure the performance of the sensor and the accuracy of measurement. | Use the temperature sensor included in the MPU-6050 to monitor whether the temperature is within the range.
Make sure there is enough pin space to connect the module | In the process of circuit design, consider the distribution of the pin connection between the sensor module and other modules.
Requirement & Verification
5

## Slide 23
Accelerometer Module
5
Why Acceleration?
F = m*a
Kalman Filter Function
Threshold-based Algorithm

## Slide 24
Flow Chart
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618

## Slide 25
Filter
Segmentation
Classification
Display
Server

## Slide 26
Eliminate the influence caused by these acceleration, deceleration, and turning, which is unrelated to road quality
Filtering Subsystem
Requirement | Verification
The abnormal pattern in the signal sequence should not be caused by the activity unrelated to road quality. | We will get the signal from accelerometer when the vehicle does acceleration, deceleration, and turning. Compare the signal sequence before and after applying the filter.
The abnormal pattern caused by the potential road quality problems should not be eliminated. | We will get the signal from accelerometer when the vehicle run on the convex and concave road. Compare the signal sequence before and after applying the filter.
1
Requirement & Verification
Apply high-pass filter

## Slide 27
Segmentation Subsystem
2
Split Into Segments
We need to report the road segment to have problems or not instead of the whole road, so we need to split the signal sequence into segments.
Preprocess
If all the segmentations will be processed by the Classification Module, it will create great load to system. We need to exclude the segments, which is unlikely to be related to bad road quality with a low-cost method.
Threshold of speed and RMS of segment can be applied.
Requirement & Verification
Requirement | Verification
Every signal segment should be corresponding to the road segment with the same length. An algorithm that converts the signal from GPS and accelerometer to speed information is necessary. | We will record the speed and distance of running vehicle. Then use the information from GPS and accelerometer to calculate speed and distance. Verify the accuracy of the algorithm by comparing the recorded value and calculated value.
The preprocess system, which excludes the segments unlikely to be related to bad road quality, should exclude negative sample as much as possible, in the condition that no positive sample will be excluded. | The threshold should make the False negative to be 0. In this situation, test different threshold that has the greatest precision.
The load of Segmentation Module should not be high. In other word, the preprocess algorithm should not be too complex. | We will compare the time cost before and after applying the exclusion algorithm. The time cost should be significantly reduced.

## Slide 28
Classification Subsystem
A machine learning based classification nodule is applied to classify the road to be safe or not.
3
Requirement | Verification
A method of feature extraction should be chosen to make the abnormal pattern can be more easily recognized by model. | We will try different methods of feature extraction to signal from the accelerometer. The abnormal pattern should be obvious from the view of people.
The training set, which has high quantity and variety should be collected. | We will make sure the number of samples is sufficient. In addition, the signal cause from various type of road quality problems should be collected.
The model should have high accuracy. | The model should have high accuracy.
The model should run in a limited time. | Every segmentation should be processed within 0.1 s. In this situation, a test set with 1000 sample should be processed by model within 100s.
Requirement & Verification

## Slide 29
Display Subsystem
Requirement | Verification
The mapping from longitude and latitude to nodes need to be accurate. | We will get the map of Haining as the map to be marked. Then we will carry our GPS sensor to run along the roads in Haining. We will choose several road segments to test. Get the signal from GPS sensor and use GPS app from phone to mark where we record the signal. Use our display subsystem to see whether the node calculated from signal of GPS sensor match the node we recorded by GPS app from phone.
Requirement & Verification
4
The longitude and latitude will be transformed into nodes on the map. The label from classification subsystem will be marked as the color of the nodes. In this situation, people can easily know which road segments is likely to have road quality problems.

## Slide 30
Flow Chart
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618

## Slide 31
Part 04
Analysis
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB974DA658112395338783245C025A59995FB9E16632CCFAA0B432708CE5F45C8C42BB719BDFBEC94DA7A649C287EAE079169C97C71560C476F719A25EEB755DC5

## Slide 32
Cost Analysis
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618
Name | Description | Cost per unit | Number | Others
MPU6050 | Sensors Module | ￥13 | 1 | N/A
ESP8266 | Wi-Fi Module | ￥28 | 1 | N/A
NEO-6M | GPS Module | ￥42 | 1 | N/A
Stm32F103C8T6 | Control Module | ￥11.3 | 1 | N/A
18650 Battery | 5V | ￥45.9 | 2 | N/A
Resistor | N/A | ￥0.02 | 10 | N/A
Capacitor | N/A | ￥0.03 | 10 | N/A
Hardware Component Cost Analysis
Device | Description | Cost per unit | Rent Hour | Total Cost
Rent Bicycle | Tested Vehicle | ￥2/hour | 30 | ￥60
Mechanical Component Cost Analysis

## Slide 33
Cost Analysis
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618
Name | Hourly Wage | Total Hour | Total Cost | Other
Yuhang Chen | ￥90 | 120 | ￥10800 | N/A
Yichen Li | ￥90 | 120 | ￥10800 | N/A
Jingyao Dai | ￥90 | 120 | ￥10800 | N/A
Yihang Yang | ￥90 | 120 | ￥10800 | N/A
Labor Component Cost Analysis
Software Component Cost Analysis
Name | Description | Cost per Unit | Number | Others
Server Rent | Vlutr | $5 | 1 | Per month

## Slide 34
Schedule
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618
Week | Content | Member
3/21-4/3 | Sensor testing | Zhengwei Dai
 | Server design | Yuhang Chen
 | Methods of feature extraction collection | Yihang Yang
 | Model collection | Yichen Li
 | Design Document and Design Review | Team
4/4-4/10 | Connection between sensor and microcontroller | Zhengwei Dai
 | WIFI module building | Yuhang Chen
 | Design filtering and segmentation subsystem | Yihang Yang
 | Data collection test | Yichen Li
 | Microcontroller Programming | Team
4/11-4/17 | Detailed PCB design | Zhengwei Dai
 | Establishing connection between PCB and server | Yuhang Chen
 | Result presentation design | Yihang Yang
 | Model implementation design | Yichen Li
4/18-4/24 | PCB building | Zhengwei Dai
 | Plan for data set collection and labeling | Yuhang Chen
 | Filtering and Segmentation subsystem implementation on server | Yihang Yang
 | Model implementation design on server | Yichen Li
4/25-5/1 | PCB debugging | Zhengwei Dai
 | Data set collection and labelling | Yuhang Chen
 |  | Yihang Yang
 |  | Yichen Li
5/2-5/8 | PCB debugging | Zhengwei Dai
 | Server maintenance | Yuhang Chen
 | Filtering and Segmentation subsystem assessment | Yihang Yang
 | Classification model assessment | Yichen Li
5/9-5/15 | PCB debugging | Zhengwei Dai
 | Server maintenance | Yuhang Chen
 | Classification subsystem optimization and debugging | Yihang Yang
 |  | Yichen Li
5/16-5/22 | Final testing and debugging Prepare for presentation | Zhengwei Dai
 |  | Yuhang Chen
 |  | Yihang Yang
 |  | Yichen Li

## Slide 35
CLICK HERE TO ADD YOUR TITLE
为客户提供有效服务，是我们工作的方向和价值评价的标尺，成就客户就是成就我们自己。
为客户提供有效服务，是我们工作的方向和价值评价的标尺，成就客户就是成就我们自己。
为客户提供有效服务，是我们工作的方向和价值评价的标尺，成就客户就是成就我们自己。
为客户提供有效服务，是我们工作的方向和价值评价的标尺，成就客户就是成就我们自己。
为客户提供有效服务，是我们工作的方向和价值评价的标尺，成就客户就是成就我们自己。为客户提供有效服务，是我们工作的方向和价值评价的标尺，成就客户就是成就我们自己。
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB77E2D09FF131CC59D0517FC127133DA2BCA9EEA6E7378E57346A9496F0D3A597577DECE229E967C8B0249DD763E024C8B850CA8EC35B74133B76747CA9531618

## Slide 36
物联网悄然改变世界的格局
The spring and autumn period and the visual studio is one of the enterprises and individuals to provide professional creativity, brand integration design consultants, more than 15 years working experience. To customers as the benchmark, with wisdom grafting business and the arts.
e7d195523061f1c01ef2b70529884c179423570dbaad84926380ABC1F97BAEF0C8FC051856578EAB7874501A1FFE158C4981707381814BCC4D9A8E3554438DEE4FBCF5A5B4D2A8B0989AB57E8BAC65EB974DA658112395338783245C025A59995FB9E16632CCFAA0B432708CE5F45C8C42BB719BDFBEC94DA7A649C287EAE079169C97C71560C476F719A25EEB755DC5
演讲：
李氏春秋
THANKS